## Slide 1: Safety & Tool ID Exam
Ag Mechanics & Metal Technology

## Slide 2: Question # 1
Name
  Table Saw
What it does
  Cuts straight lines in wood
Safety rules
  2 people to use it
  3 teeth above
  Use push stick if close to fence
  Stand to the side of blade
  Never have fingers in line with blade

## Slide 3: Question # 3
Name
  Portable hand drill
What it does
  Drill holes in wood or metal
Safety rules
  Carry pointed down
  Don’t pull trigger unless your using tool
  Pull trigger all the way down when using it

## Slide 4: Question #4
Name
  Wood Rasp
What it does
  Removes a lot of wood when smoothing
Safety rules
  Carry pointed down

## Slide 5: Question # 5
Name
  Circular Saw
What it does
  Cuts straight lines in wood
Safety rules
  Clamp wood down
  Know what is under wood
  Watch chord
  Start machine with blade not touching wood

## Slide 6: Question # 6
Name
  Claw Hammer
What it does
  Drives and removes nails
Safety rules
  Don’t swing above head
  Don’t hit against another hammer

## Slide 7: Question # 7
Name
  Drill Press
What it does
  Drills holes in wood or metal
Safety rules
  No loose clothing/hair tied back/etc
  Chuck must be in its home
  Clamp material down
  Keep piece of scrap wood below what you are drilling

## Slide 8: Question # 8
Name
  Level
What it does
  Checks to see if things are level (parallel with ground) or straight up and down

## Slide 9: Question # 9
Name
  Miter Saw
What it does
  Cuts angles in wood
Safety rules
  Watch your thumb
  Keep wood against fence
  When pulling the trigger hold till blade is all the way down and back up before releasing
  Keep finger off trigger until ready to use
  Don’t cross arms

## Slide 10: Question # 10
Name
  Speed Square
What it does
  Measures angles and makes drawing 90 and 45 degree angles easy

## Slide 11: Question # 11
Name
  Band Saw
What it does
  Cuts curved lines in wood
Safety rules
  Don’t cut cylindrical/round material
  Fingers should not be in line with blade
  Clear scrap with piece of wood
  Never make adjustments inside machine while it’s plugged in
  If you hear a pop turn machine off and grab Molina

## Slide 12: Question # 13
What it is
Metal File
What it does
Smoothes Metal
Safety Rule
Carry pointed down

## Slide 13: Question # 14
Name
  Vise Grip
What it does
  Holds hot metal securely

## Slide 14: Question #15
15a*
Flathead screwdriver
15b*
  Phillips Head Screwdriver
  Carry both pointed down

## Slide 15: Question # 17
What it is
  Needle Nose Pliers

## Slide 16
Name
  Channel Locks
What it does
  Helps Tighten and Loosen

## Slide 17
Name
  Ratchet and Socket
What it does
  Helps Tighten and Loosen nuts and bolts

## Slide 18
Name
  Chipping (slag) hammer
What it does
  Used during stick welding to remove slag

## Slide 19
Name
  Wrench
What it does
  Helps Tighten and Loosen nuts and bolts

## Slide 20
Name
  Vise
What it does
  Holds things securely (usually metal)
Safety rules
  Don’t over tighten
  Make sure to close when done using

## Slide 21
Name
  Drill Bits (individually)
  Drill Bit Index (the whole box)
What it does
  Drills holes in different materials

## Slide 22
Name
  Ball Peen Hammer
What it does
  Hammers everything but nails
Safety rules
  Don’t swing above head
  Don’t hit against another hammer or hardened material